## Slide 1
CPS Framework Ontology Use-Cases, Formalization and
Reasoning Examples
M. Balduccini and C. Vishik
November 3, 2017

## Slide 2: Progress
Done:
  Need to include all of the components in the system diagrams
  Revise use-case descriptions for examples 2-3
    Automotive/Cam - Lane Keeping/Assist
    Automotive/Sensors - Adaptive Cruise Control
    Check colors and line-styles
  Generalized CPS diagram created
    Example 1-3 diagrams are instances of it
  Alignment of the properties/requirements to the correct Framework concern
  Alignment of requirements for cybersecurity
  Exposing clearly the interactions between the concerns
  In properties, use superscript to show concern
  In constraints/dependencies/trade-offs, use
  Single level of decomposition considered

## Slide 3: Progress
To do:
  Review choices with team
  Create graph(s) for the ontology
  Create graph(s) for constraints/dependencies/trade-offs
  Update prototype
  Replace screenshots
  Multiple levels of decomposition
    Querying for all properties for a given concern, at all levels of decomposition

## Slide 4: Goals
Demonstrate
  Formalization of CPS Model and surrounding domain
  Formalization of attacks, their effects, mitigation actions
  Reasoning about aspects, concerns, properties
    Recursive traversal of concern trees
  Reasoning about physical ramifications
  Finding mitigations, reasoning about their effects

## Slide 5: Formalization

## Slide 6: Goals of the Formalization
Capture relevant knowledge about a CPS
  CPS-independent: Aspects/Concerns hierarchy
  CPS-specific: Properties
  Constraints, dependencies, tradeoffs
    General-purpose, e.g. thermodynamics
    CPS-specific, e.g.:
      Component dependencies
      Property dependencies
      Effects of malware
Enable reasoning about:
  The current state of the CPS
    Both logical and physical
  Which Properties are violated
  Which Aspects/Concerns are currently satisfied
  How to reach a desired state
    Recovery to mission capability

## Slide 7: Proposed Formalization Components
Aspect/Concern hierarchy
Properties
  Each concern is associated with a set of properties
    : property of concern
  Each property is represented by an atomic statement
    Case 1: truth value is not specified
      “Camera is capable of recording at 25 fps”
    Case 2: truth value is specified must be satisfied for concern to be satisfied
      “Camera uses encrypted memory”
  Will later include continuous features
: set of properties of concern
Within CPS Framework

## Slide 8: Proposed Formalization Components
Configuration of the CPS
  Provides us with the truth value of atomic statements
    “Basic camera is in use”
    “Basic camera is currently using encrypted memory and recording at 50 fps”
Constraints, dependencies, trade-offs
  Provide us with dependencies among atomic statements (properties + configuration)
    “It is impossible for basic camera to use encrypted memory while recording at 50 fps”
    “If basic camera uses encrypted memory while recording at 30+ fps, average frame drop rate is 25%” or “… is ”
  Describe how actions affect the configuration of the CPS
  Recursively affect satisfaction of concerns, aspects
Possible general form
Beyond CPS Framework
One conclusion: negative interaction between confidentiality and functionality

## Slide 9: Generalized Diagram
camera
mic
indicator
SAM
integrated body security system
vf2
Message: byte seq.
Information: videofeed
contains vf1
encoding AES
af2
Message: byte seq.
Information: audiofeed
contains af1
encoding AES
cmd1
Message: command packet
Information: type of warning, attributes
vf1
Influence: video signal
Energy: electr. waves
af1
Influence: audio signal
Energy: sound waves
storage
avf1
Message: byte seq.
Information: combined videofeed, audiofeed
contains vf2
contains af2
encoding AES
operating environment
remote station
alarm1
Message: alarm packet
Information: type of alarm, timestamp, location, officer ID
robotic camera
targeting
mech
o1
Influence: angle change
Energy: mechanical
cmd2
Message: command packet
Information: degrees, speed
integrated body security system (stand-alone part)
user
Physical connection
Direct logical connection
Physical element
Logical element
Physical & logical system
Description of interaction
Annotation
text
text
ws1
Influence: warning signal
Energy: waves TBD
consumer
avf2
Influence: audio, video signals
Information: sound, light waves
Generalization of the diagrams for Examples 1-3
“Parametrized” components circled in red

## Slide 10: Summary of Examples
Simplified “Body Camera”
  Camera
  SAM
  Minimal assumptions on knowledge about connections
  Link to broader domain: admissibility of video in court
Self-Driving Car (a)
  Camera
  SAM
  Broader domain: consequences on car’s operations
Self-Driving Car (b)
  Sensors
  SAM
  Broader domain: consequences on car’s operations

## Slide 11: Example 1 Body Camera
An integrated body security system for situational awareness and safety of security personnel

## Slide 12: Example 1 “BodyCam” Diagram
camera
mic
indicator
SAM
integrated body security system
vf2
Message: byte seq.
Information: videofeed
contains vf1
encoding AES
af2
Message: byte seq.
Information: audiofeed
contains af1
encoding AES
cmd1
Message: command packet
Information: type of warning, attributes
vf1
Influence: video signal
Energy: electr. waves
af1
Influence: audio signal
Energy: sound waves
storage
avf1
Message: byte seq.
Information: combined videofeed, audiofeed
contains vf2
contains af2
encoding AES
operating environment
command center
alarm1
Message: alarm packet
Information: type of alarm, timestamp, location, officer ID
robotic camera
targeting
mech
o1
Influence: angle change
Energy: mechanical
cmd2
Message: command packet
Information: degrees, speed
integrated body security system (stand-alone part)
officer
Physical connection
Direct logical connection
Physical element
Logical element
Physical & logical system
Description of interaction
Annotation
text
text
ws1
Influence: warning signal
Energy: waves TBD
court
avf2
Influence: audio-video signal
Information: sound, light waves

## Slide 13: Example 1 Simplified “BodyCam”
Actors
  Camera
    Basic camera
    Advanced camera
    Two modes:
      Record at 25 fps
      Record at 50 fps
    Security features (may be enabled)
      Encrypted memory
      Secure boot
  SAM (Situational Awareness Module)
    SAM controls the recording rate
MUST UPDATE AFTER DIAGRAM IN PREVIOUS SLIDE IS CHECKED

## Slide 14: Aspects, Concerns, Properties
Trustworthiness Elements
Safety
Reliability
Security
Physical security
Confidentiality
Integrity
Availability
Privacy
Resilience
Cybersecurity
Functionality
Functional
Timing
Time-interval and latency control
Aspects
Concerns
Camera does not drop frames
SAM uses secure boot
Camera uses sec. boot
Camera should be capable of recording at 25 fps or at 50 fps
SAM uses encrypted memory
Camera uses encrypted memory
Note: unless otherwise specified, “camera” refers to both basic and advanced camera

## Slide 15: Formalization
Trustworthiness Elements
Safety
Reliability
Security
Physical security
Confidentiality
Integrity
Availability
Privacy
Resilience
Cybersecurity
Functionality
Functional
Timing
Time-interval and latency control
Aspects
Concerns
Aspect/Concern Trees

## Slide 16: Formalization
Trustworthiness Elements
Safety
Reliability
Security
Physical security
Confidentiality
Integrity
Availability
Privacy
Resilience
Cybersecurity
Functionality
Functional
Timing
Time-interval and latency control
Aspects
Concerns
Aspect/Concern Trees
Functionality Concern
Camera will not drop frames
MUST UPDATE ENCODING AND SCREENSHOTS

## Slide 17: Formalization
Trustworthiness Elements
Safety
Reliability
Security
Physical security
Confidentiality
Integrity
Availability
Privacy
Resilience
Cybersecurity
Functionality
Functional
Timing
Time-interval and latency control
Aspects
Concerns
Aspect/Concern Trees
Functionality Concern
Camera will not drop frames
Integrity Concern
SAM is capable of using secure boot
Camera is capable of using sec. boot
MUST UPDATE ENCODING AND SCREENSHOTS
MUST UPDATE ENCODING AND SCREENSHOTS

## Slide 18: Example 1
System Configuration
  SAM and camera use encrypted memory and secure boot
  Basic camera is used
  Recording rate set at 25 fps by SAM
MUST UPDATE

## Slide 19: Example 1
Constraints, Dependencies, Trade-offs
  “When the basic camera is in use, using encrypted memory and recording at 50 fps impacts negatively the dropping of frames”
MUST UPDATE

## Slide 20: Example 1
System Configuration
  SAM and camera use encrypted memory and secure boot
  Basic camera is used
  Recording rate set at 25 fps by SAM
Questions
  Is the integrity concern satisfied?
MUST UPDATE

## Slide 21: Example 1
System Configuration
  SAM and camera use encrypted memory and secure boot
  Basic camera is used
  Recording rate set at 25 fps by SAM
Questions
  Is the integrity concern satisfied?
  Outcome of the reasoning process:
Integrity concern is satisfied
Trustworthiness concern tree (fragment)
MUST UPDATE

## Slide 22: Example 1
System Configuration
  SAM and camera use encrypted memory and secure boot
  Basic camera is used
  Recording rate set at 25 fps by SAM
Questions
  Is the trustworthiness aspect satisfied?
  Outcome of the reasoning process:
Trustworthiness aspect is satisfied
Trustworthiness concern tree

## Slide 23: Example 1
System Configuration
  SAM and camera use encrypted memory and secure boot
  Basic camera is used
  Recording rate set at 25 fps by SAM
Questions
  Are all aspects satisfied?
  Outcome of the reasoning process:
All aspects are satisfied
Trustworthiness concern tree
MUST UPDATE

## Slide 24: Example 1
Also tested:
  Adding properties for timing aspect
  Elaborating other properties
  Manually disabling encrypted memory, secure boot on SAM and/or camera
  Asking questions about functional, timing aspects and their concerns
MUST UPDATE

## Slide 25: Example 1 – Step 2
System Configuration
  SAM and camera use encrypted memory and secure boot
  Basic camera is used
  Recording rate set at 25 fps by SAM
A cyberattack occurs and hacks the SAM to activate recording at 50 fps
Approximate First-Order Logic equivalent:
MUST UPDATE

## Slide 26: Example 1 – Step 2
System Configuration
  SAM and camera use encrypted memory and secure boot
  Basic camera is used
  Recording rate set at 25 fps by SAM
A cyberattack occurs and hacks the SAM to activate recording at 50 fps
Questions
  Is the integrity concern satisfied?
  Outcome of the reasoning process:
Integrity concern is not satisfied
Trustworthiness concern tree (fragment)
MUST UPDATE
MUST UPDATE

## Slide 27: Example 1 – Step 2
System Configuration
  SAM and camera use encrypted memory and secure boot
  Basic camera is used
  Recording rate set at 25 fps by SAM
A cyberattack occurs and hacks the SAM to activate recording at 50 fps
Questions
  Is the trustworthiness aspect satisfied?
  Outcome of the reasoning process:
No
Trustworthiness concern tree
MUST UPDATE

## Slide 28: Example 1 – Step 2
System Configuration
  SAM and camera use encrypted memory and secure boot
  Basic camera is used
  Recording rate set at 25 fps by SAM
A cyberattack occurs and hacks the SAM to activate recording at 50 fps
Questions
  What happens in the environment?
  Outcome of the reasoning process:
The recording is thrown out of court
because data integrity was violated
Conclusion based on the knowledge:
MUST UPDATE

## Slide 29: Example 1 – Step 3
System Configuration
  SAM and camera use encrypted memory and secure boot
  Basic camera is used
  Recording rate set at 25 fps by SAM
A cyberattack occurs and hacks the SAM to activate recording at 50 fps
Questions
  How can it be mitigated?
Approximate First-Order Logic equivalent:
for every action
Mitigation Generation Module:

## Slide 30: Example 1 – Step 3
System Configuration
  SAM and camera use encrypted memory and secure boot
  Basic camera is used
  Recording rate set at 25 fps by SAM
A cyberattack occurs and hacks the SAM to activate recording at 50 fps
Questions
  How can it be mitigated?
  Outcome of the reasoning process:
All aspects are satisfied
“Replace basic camera with
advanced camera”
MUST UPDATE

## Slide 31: Example 2 Self-Driving Car (a)
A self-driving car uses SAM and camera for lane keeping/assist

## Slide 32: Example 2 Self-Driving Car (a)
camera
mic
indicator
SAM
integrated body security system
vf2
Message: byte seq.
Information: videofeed
contains vf1
encoding AES
af2
Message: byte seq.
Information: audiofeed
contains af1
encoding AES
cmd1
Message: command packet
Information: type of warning, attributes
vf1
Influence: video signal
Energy: electr. waves
af1
Influence: audio signal
Energy: sound waves
storage
avf1
Message: byte seq.
Information: combined videofeed, audiofeed
contains vf2
contains af2
encoding AES
operating environment
remote assit
alarm1
Message: alarm packet
Information: type of alarm, timestamp, location, officer ID
robotic camera
targeting
mech
o1
Influence: angle change
Energy: mechanical
cmd2
Message: command packet
Information: degrees, speed
integrated body security system (stand-alone part)
driver
Physical connection
Direct logical connection
Physical element
Logical element
Physical & logical system
Description of interaction
Annotation
text
text
ws1
Influence: warning signal
Energy: waves TBD
steering wheel
ctrl1
Message: angle change
Information: mechanical

## Slide 33: Example 2: Self-Driving Car (a)
A self-driving car uses SAM and camera for lane keeping/assist
Actors
  Camera
    Basic camera
    Advanced camera
    Two modes:
      Record at 25 fps
      Record at 50 fps
    Security features (may be enabled)
      Encrypted memory
      Secure boot
  SAM (Situational Awareness Module)
    SAM controls the recording rate
engine
control
MUST UPDATE

## Slide 34: Example 2: Self-Driving Car (a)
System Configuration
  SAM and camera use encrypted memory and secure boot
  Basic camera is used
  Recording rate set to 25 fps by SAM
A cyberattack occurs and hacks the SAM to activate recording at 50 fps
Questions
  Is the integrity concern satisfied?
  Is the trustworthiness aspect satisfied?
  What are the physical ramifications?
  How can it be mitigated?
“Replace the basic camera with the advanced camera”
Conclusion based on the knowledge:
MUST UPDATE
MUST UPDATE
MUST UPDATE

## Slide 35: Example 3 Self-Driving Car (b)
A self-driving car uses SAM and sensors for adaptive cruise control

## Slide 36: Example 2 Self-Driving Car (b)
camera
mic
indicator
SAM
integrated body security system
vf2
Message: byte seq.
Information: videofeed
contains vf1
encoding AES
af2
Message: byte seq.
Information: audiofeed
contains af1
encoding AES
cmd1
Message: command packet
Information: type of warning, attributes
vf1
Influence: video signal
Energy: electr. waves
af1
Influence: audio signal
Energy: sound waves
storage
avf1
Message: byte seq.
Information: combined videofeed, audiofeed
contains vf2
contains af2
encoding AES
operating environment
remote assit
alarm1
Message: alarm packet
Information: type of alarm, timestamp, location, officer ID
robotic camera
targeting
mech
o1
Influence: angle change
Energy: mechanical
cmd2
Message: command packet
Information: degrees, speed
integrated body security system (stand-alone part)
driver
Physical connection
Direct logical connection
Physical element
Logical element
Physical & logical system
Description of interaction
Annotation
text
text
ws1
Influence: warning signal
Energy: waves TBD
accelerator
ctrl1
Influence: angle change
energy: mechanical
brake
ctrl2
Influence: angle change
energy: mechanical

## Slide 37: Example 3: Self-Driving Car (b)
A self-driving car uses SAM and sensors for adaptive cruise control
Actors
  Sensors
    Interpolating sensors (inaccurate hardware, interpolation compensates)
    Non-interpolating sensors (accurate hardware)
  SAM (Situational Awareness Module)
    SAM requests sensor readings either at low rate or high rate
    In interpolating sensors:
      High request rate causes interpolation to be cut short
      Potentially leads to inaccurate data returned to SAM

## Slide 38: Example 3: Self-Driving Car (b)
System Configuration
  SAM and sensors use encrypted memory and secure boot
  Interpolating sensors are used
  SAM requests sensor readings at low rate
Questions
  Is the integrity concern satisfied?
  Is the trustworthiness aspect satisfied?
  Are all aspects satisfied?

## Slide 39: Example 3 – Step 2
System Configuration
  SAM and sensors use encrypted memory and secure boot
  Interpolating sensors are used
  SAM requests sensor readings at low rate
A cyberattack occurs and hacks the SAM to request readings at a high rate
Questions
  Is the integrity concern satisfied?
  Is the trustworthiness aspect satisfied?
  What are the physical ramifications?
Conclusion based on the knowledge:

## Slide 40: Example 3 – Step 3
System Configuration
  SAM and sensors use encrypted memory and secure boot
  Interpolating sensors are used
  SAM requests sensor readings at low rate
A cyberattack occurs and hacks the SAM to request readings at a high rate
Questions
  Is the integrity concern satisfied?
  Is the trustworthiness aspect satisfied?
  What are the physical ramifications?
  How can it be mitigated?
Mitigation Generation Module
“Replace interpolating sensors
with non-interpolating ones”
MUST UPDATE
MUST UPDATE

## Slide 41: Example 3 (Variant) Multiple Possible Mitigations

## Slide 42: Example 3 – Step 3 (Extended)
System Configuration
  SAM and sensors use encrypted memory and secure boot
  Interpolating sensors are used
  SAM requests sensor readings at low rate
A cyberattack occurs and hacks the SAM.
Unless a patch is applied, the SAM will request readings at a high rate.
Questions
  Is the integrity concern satisfied?
  Is the trustworthiness aspect satisfied?
  What are the physical ramifications?
  How can it be mitigated?
Solution #1
Solution #2
Effect of mitigation
“Patch the SAM”
MUST UPDATE
MUST UPDATE

## Slide 43: Conclusions
Demonstrated
  Formalization of CPS Model and surrounding domain, attacks, mitigations
  Reasoning about concerns, properties, physical ramifications
  Finding (multiple) mitigations, reasoning about their effects
  Three examples: “BodyCam”, Self-driving Car (a & b)
  Next Steps
  Standardization of modeling of surrounding domain, attacks, mitigations
  Parametrization of properties
  Formalization, leverage of knowledge about CPS structure